## Slide 1: BIRDS-5
Weekly Update for Communication, S&F, and Antenna Subsystems
Anechoic Chamber Test
07-January-2021
Ramson Nyamukondiwa
Edgar Mujuni

## Slide 2: Outline
Antenna Tuning
Antenna Radiation Pattern
Sensitivity Testing

## Slide 3: Test1: Antenna Tuning=> S11 Parameters
  Three 1U satellites and one 2U satellite
  Results in dB log curve and Smith Chat
          Calibration UHF (435-438 MHz)
          Calibration VHF (144-146MHz)

## Slide 4
VHF S-parameter 1U Satellite
S11 – -20.3dB
Freq – 145MHz

## Slide 5
UHF S-parameter 1U Satellite
S11 – -20.2dB
Freq – 435MHz
Length - 193mm

## Slide 6
UHF S-parameter Sat4: 2U
S11 – -26.4dB
Freq – 435MHz

## Slide 7: Test – 2 : Measuring Dipole Antenna Radiation Pattern
One 1U and one 2U
UHF and VHF antenna pattern :
  E and H planes
  Determine the antenna gain

## Slide 8
Radiation Pattern Measurement procedure
Measure all the cable losses for each frequency (145MHz & 437MHz)
Calculate ideal Path Loss at 3.71m
Measure the path loss from Spectrum Analyzer reading using Ref. Antenna
Compare the path loss results & confirm them to be almost equal.
Conduct Radiation patten measurement of Ref Antenna (Gmax should be around 2.2dBi)
Replace Reference Antenna with Satellite antenna (Satellite)
Conduct Radiation pattern measurement of Satellite Antenna.

## Slide 9
E-plane
H-plane
VHF Reference Antenna
Gmax – 2.4dBi

## Slide 10
E-plane
H-plane
VHF 1U – Satellite
Gmax – 1.4dBi

## Slide 11
E-plane
H-plane
VHF 2U Satellite
Gmax – 1.6dBi

## Slide 12
E-plane
H-plane
UHF 1U - Satellite
Gmax – 1.9dBi

## Slide 13
E-plane
H-plane
UHF : 2U Satellite
Gmax : 1.8dBi

## Slide 14: Test – 3 : Measuring TRX Sensitivity
UHF Transceiver Sensitivity=>ADD1397BF
VHF Transceiver Sensitivity => BiM1H
Preparations
  Battery Voltage
  CW and FM Output Power

## Slide 15: Test – 3 : Measuring TRX Sensitivity
Calibration
  Measure cable loses in Up and Downlink
  Measuring the ICOM radio transmission power
  Determine the practical antenna gains of
    Ref Antenna and BIRDS antenna
  Determine the path loss for Up and Downlink
  Measure received power at the antenna
Uplink success rate

## Slide 16: Summary of Measured Output Power
Satellites and Transceivers Used | Battery Voltage (V) | CW TX Output (dBm) | FM TX Output (dBm)
Satellite1 Transceiver 1: New | 4.1 | 25.3 | 28.8
Satellite 2 Transceiver 2: BIRDS4 | 4.1 | -17.1 | -30.0
Satellite 3 Transceiver 3: BIRDS3 | 4.1 | 20.8 | 28.7
Satellite 4 Transceiver 4: 2U Only | 4.0 | 20.2 | 28.8
FM and CW output were measured with power meter

## Slide 17: Calibration-UHF
Attenuator
ICOM-9100 Radio
39 dB
Radio Transmission Output
2. Cable Loss
Signal Generator
Spectrum analyzer
Spectrum analyzer
3. Attenuator Functionality Checked
Variable Attenuations
Only verified Attenuators were used

## Slide 18: Determining the Path Loss
Attenuator
ICOM-9100 Radio
39 dB
Spectrum analyzer
Ref Ant: =2.15dBi,
Att=9.9 dB
Ref Ant: =2.15dBi,
Att=9.9 dB
Practical Path Loss
= 38.2dB
2. Theoretical/Ideal Path Loss
= 36.74dB
Where: , c: Speed of light, d: distance between the two antennas

## Slide 19: Confirming Power at the Receiving Side
The UHF antennas for three satellites gave similar received power at the antenna
Maximum difference of 0.6dBm hence similar performance.
Satellite 2 antenna became lossy
Satellite | 
1 | -98.2 dBm
2 | -90.5dBm
3 | -98.9 dBm
4 | -98.4 dBm
Variable Attenuations
ICOM-9100 Radio
Spectrum analyzer
Satellite
Ref Ant: =2.15dBi,
Att=9.9 dB

## Slide 20: Testing the Antenna Gain in UHF Uplink
Rx Antenna | Prx (dBm) | Antenna Gain
Ref Dipole Antenna with 9.9 dB attenuation | -55.7dBm | 2.15 dBi
BIRDS 5 Dipole Antenna Satellite 1 | -98.2 dBm | 1.45 dBi
Measured and verified with Radio setup
SA: Noise floor= -120 dBm

## Slide 21: Antenna Gain in UHF Downlink
Rx Antenna | Antenna Gain
Ref Dipole Antenna with 9.9 dB attenuation | 2.15 dBi
BIRDS 5 Dipole Antenna 1 | 1.9 dBi
BIRDS 5 Dipole Antenna 4 | 1.8 dBi
Measured and verified with SG setup
SA: Noise floor= -120 dBm
From the radiation Pattern

## Slide 22: Received Power Measurements in Uplink (Setup Calibration)
Variable Attenuation(dB) | Effective Att (dB) | Expected Prx using SAT Antenna(dBm) | Measured Prx using Sat Antenna (dBm)
39 | -91.1 | -55.2 | -55.7
69 | -121.1 | -85.2 | -85.0
79 | -131.1 | -95.2 | -95.3
82 | -134.1 | -98.2 | -98.0
84 | -135.1 | -100.2 | -100.6
85 | -136.1 | -101.2 | -101.0

## Slide 23: Measuring UHF TRX Sensitivity
Satellite
UHF Dipole Antenna
Variable Attenuators
ICOM-9100 Radio
TNC
47dBm

## Slide 24: Measuring UHF TRX Sensitivity
Door-1
Door-2
Door-3
Anechoic chamber
Satellite
Reference antenna
GS
Ground station Location

## Slide 25: Sensitive Testing UHF
Variable Attenuation(dB) | Effective Att (dB) | Expected Prx using SAT Antenna | Success Rate TRX1: New (Decoded) | Success Rate TRX2: BIRDS4 (Decoded) | Success Rate TRX3: BIRDS3 (Decoded) | Success Rate TRX4: 2UOnly (Decoded)
39 | -91.1 | -55.2 | 6/6 | 6/6 | 6/6 | 6/6
69 | -121.1 | -85.2 | 6/6 | 0/6 | 6/6 | 6/6
79 | -131.1 | -95.2 | 6/6 | 0/6 | 6/6 | 6/6
81 | -133.1 | -97.2 | 5/6 | 0/6 | 6/6 | 6/6
82 | -134.1 | -98.2 | 5/6 | 0/6 | 6/6 | 5/6
83 | -135.1 | -99.2 | 5/6 | 0/6 | 6/6 | 5/6
84 | -136.1 | -100.2 | 4/6 | 0/6 | 6/6 | 3/6
85 | -137.1 | -101.2 | 3/6 | 0/6 | 6/6 | 0/6
88 | -140.1 | -104.2 | 1/6 | 0/6 | 4/6 | 0/6
The test was repeated two different times and we verified the same results

## Slide 26: Sensitivity of Satellite2: BIRDS4-TRX
Variable Attenuation(dB) | Effective Att (dB) | Expected Prx using SAT Antenna | Success Rate |  | 
 |  |  | Decoded | Received but not Decoded | Not Received
39 | -91.1 | -55.2 | 6/6 | 0/6 | ---
40 | -92.1 | -56.2 | -- | 6/6 | --
54 | -106.1 | -70.2 | -- | 5/6 | --
55 | -107.1 | -71.2 | -- | 4/6 | --
56 | -108.1 | -72.2 | -- | 4/6 | --
57 | -109.1 | -73.2 | -- |  | 6/6
BIRDS 4 Transceiver has very low Sensitivity

## Slide 27: Comparison of BIRDS Sensitivity
BIRDS5 |  |  |  | 
 | TRX1: New | TRX2: BIRDS4EM | TRX3: BIRDS3EM | TRX4: 2U
EM (dBm) | -- | -- | -103 | -101
FM (dBm) | -101.2 | -72 | -104.2 | -100.2

## Slide 28: Test Conclusion for UHF TRX Sensitivity
Transceivers Tested | Uplink | Downlink | Overall Comment
Transceiver1: New | Good | Good | Good
Transceiver2: BIRDS4 | Good | Not Good | Not Good
Transceiver3: BIRDS3 | Good | Good | Good
Transceiver4: 2U Only | Good | Good | Good

## Slide 29: Calibration-VHF
Attenuator
Radio Transmission Output
2. Cable Loss
Spectrum analyzer
Spectrum analyzer
TH-D72A Kenwood Radio
TH-D72A Kenwood Radio

## Slide 30: Determining the Path Loss
Variable Attenuators
Spectrum analyzer
Ref Ant: =2.15dBi,
Att=9.9 dB
Ref Ant: =2.15dBi,
Att=9.9 dB
Practical Path Loss
= 26.9dB
2. Theoretical/Ideal Path Loss
= 27.1dB
Where: , c: Speed of light, d: distance between the two antennas
TH-D72A Kenwood Radio

## Slide 31: Testing the Antenna Gain in VHF Uplink
Rx Antenna | Prx (dBm) | Antenna Gain
Ref Dipole Antenna with 9.9 dB attenuation | -55.7dBm | 2.15 dBi
BIRDS 5 Dipole Antenna Satellite 1 | -86.1 dBm | 1.5 dBi
Measured and verified with Radio setup
SA: Noise floor= -120 dBm

## Slide 32: Antenna Gain in VHF Downlink
Rx Antenna | Antenna Gain
Ref Dipole Antenna with 9.9 dB attenuation | 2.2 dBi
BIRDS 5 Dipole Antenna 1 | 1.4dBi
BIRDS 5 Dipole Antenna 4 | 1.6dBi
Measured and verified with Handheld Radio setup
SA: Noise floor= -120 dBm
From the radiation Pattern

## Slide 33: Received Power Measurements in VHF Uplink (Setup Calibration)
Variable Attenuation(dB) | Effective Att (dB) | Expected Prx using SAT Antenna(dBm) | Measured Prx using Sat Antenna (dBm)
33 | -72.8 | -50.2 | -50.4
63 | -102.8 | -80.2 | -80.4
67 | -106.8 | -84.2 | -84.3
69 | -108.8 | -86.2 | -86.1
73 | -112.8 | -90.2 | -90.1

## Slide 34: Measuring VHF TRX Sensitivity
Satellite
UHF Dipole antenna
Attenuator
ICOM-9100 Radio
TNC
Test Setup
Variable Attenuators
TH-D72A Kenwood Radio
Monopole Antenna

## Slide 35: Sensitive Testing VHF
Var Att (dB) | Eff. Att (dB) | Ex Prx using SAT Ant | Succ Rate: CDR | SuccRate: B4 EM | Succ Rate: SAT1 | Succ Rate: SAT2 | SuccRate: SAT3 | Succ Rate: Sat4
69 |  | -86 | 4/4 | 4/4 | 4/4 | 4/4 | 4/4 | 4/4
70 |  | -87 | 3/4 | 1/4 | 4/4 | 4/4 | 4/4 | 4/4
71 |  | -88 | 0/4 | 0/4 | 4/4 | 4/4 | 4/4 | 4/4
73 |  | -90 | 0/4 | 0/4 | 4/4 | 4/4 | 4/4 | 4/4
75 |  | -92 | 0/4 | 0/4 | 4/4 | 4/4 | 4/4 | 4/4
79 |  | -96 | 0/4 | 0/4 | 4/4 | 4/4 | 4/4 | 4/4
80 |  | -97 | 0/4 | 0/4 | 4/4 | 4/4 | 4/4 | 0/4
81 |  | -98 | 0/4 | 0/4 | 4/4 | 4/4 | 4/4 | 0/4
82 |  | -99 | 0/4 | 0/4 | 0/4 | 0/4 | 0/4 | 0/4
83 |  | -100 | 0/4 |  | 4/4 | 4/4 | 4/4 | 4/4

## Slide 36: Comparisons
 | Sat1 | Sat2 | Sat3 | Sat4 | CDR | BIRDS 4 EM
FM | 98 | 98 | 98 | 96 |  | 
EM |  |  |  |  | 87 | 86